An Improved Integer Multiplicative Inverse (modulo 2w)

Jeffrey Hurchalla
jeffrey@jeffhurchalla.com

April 8, 2022

Abstract
     This paper presents an algorithm for the integer multiplicative inverse (mod 2w) which completes in the fewest cycles known for modern microprocessors, when using the native bit width w for the modulus 2w. The algorithm is a modification of a method by Dumas, and for computers it slightly increases generality and efficiency. A proof is given, and the algorithm is shown to be closely related to the better known Newton’s method algorithm for the inverse. Simple direct formulas, which are needed by this algorithm and by Newton’s method, are reviewed and proven for the integer inverse modulo 2k with k = 1,2,3,4, or 5, providing the first proof of the preferred formula with k=4 or 5.

# 1 Introduction

The integer multiplicative inverse (modulo 2w) of an odd integer a is the integer x that satisfies
ax equiv 1 ( mod 2^w )	(1)

where w is typically set to the bit width of arithmetic operations on a computer.

We will refer to x as simply the “multiplicative inverse” or “inverse”. The inverse x is a unique value (mod 2w) for any odd integer a, and it does not exist for any even integer a.

Applications for the inverse include Montgomery multiplication [1][16], computing exact division by an integer constant [2], testing for a zero remainder after dividing by a constant [3], and integer division [4].

The inverse can be calculated in at least three different ways. The first and most well known method is the extended Euclidean algorithm [5]. The second method is inspired by Newton’s method for approximating a reciprocal [6], and we follow a convention of simply calling it “Newton’s method”[1] [10]. The third method was discovered by Dumas [7], and is expanded upon in this paper for implementation on a computer.
[1] More accurately it is Newton’s method over p-adic numbers, or a use of Hensel lifting.

For background, calculating the inverse via Newton’s method is almost always more efficient on a computer than via the extended Euclidean algorithm. Given the modulus 2w, Newton’s method has order of complexity O(log w), as compared to O(w) for the extended Euclidean. Newton’s method also has a better constant factor in its expected running time due to the fact that it uses no divisions. Granlund and Montgomery [9] first mentioned Newton’s method for the integer inverse, Warren [10] provided an easy to follow algorithm and proof for it, and academic papers [7][11][12] and blog entries [8][13][14] further explored it.

Given the modulus 2w, Dumas’ Algorithm 3 [7] has nearly the same number and type of operations as Newton’s method. In practice however, Dumas’ algorithm can complete faster on modern CPUs because a CPU can exploit instruction level parallelism when executing it [8]. Section 6 shows its improved latency compared to Newton’s method. The algorithm in this paper further improves Dumas’ algorithm for use on a computer.

# 2 Computing the Multiplicative Inverse

We present a different derivation of Dumas’ Algorithm 3 that provides improvements to its flexibility and efficiency on a computer.

For the sake of readability, we use the expression pow(2, n) to represent an integer 2n. For example, y pow(2, n) would represent y^{2^{`n}} .

Let a be an odd integer for which we wish to find the multiplicative inverse (mod 2w).
Let w be a positive integer. In practice we set w to the bit width of the arithmetic we will use on a computer; most commonly w is 32 or 64, for a 32 bit or 64 bit computer architecture.
Let k be a positive integer such that k divides w, and such that (w/k) is a power of 2. We usually wish to use k<=5 (in order to use simple direct formulas from section 5), so if a k in that range does not exist, increase w by the minimal amount needed to obtain a satisfactory k; the algorithm’s result will suffice for your original value of w. Common choices for k would be 1, 2, or 4. We can note in advance that doubling the size of k decreases the number of iterations required by the upcoming recurrence (4) by 1.

Set x0 to any integer that satisfies
ax_0 equiv 1 `` ( mod 2^k )	(2)

Section 5 lists formulas for x0 for values of k=1, 2, or 4. For example, if we are using k=1, then x0=1 satisfies (2).

Set y to any integer that satisfies
y equiv 1 - ax rsub{0} ``( mod 2^w )	(3)

Define the discrete recurrence relation
x rsub {n+1} equiv x rsub {n} ( 1 + y rsup { pow(2, `n)} ) `` (mod 2^w)	(4)

Set p to the integer
p = log rsub{2}(w/k)	(5)

And perform p iterations of recurrence relation (4).
The resulting xp is the desired integer inverse of a, satisfying
ax rsub {p} equiv 1 `` (mod 2^w)	(6)

The following C function implements the algorithm, using w=64, k=4, and thus p=4:

1. uint64_t integer_inverse(uint64_t a)
2. {
3. assert(a%2 == 1);
4. uint64_t x0 = (3*a)^2; // See section 5, formula 3.
5. uint64_t y = 1 - a*x0;
6. uint64_t x1 = x0*(1 + y);
7. y *= y;
8. uint64_t x2 = x1*(1 + y);
9. y *= y;
10. uint64_t x3 = x2*(1 + y);
11. y *= y;
12. uint64_t x4 = x3*(1 + y);
13. return x4;
14. }

Figure 1: C code for the 64 bit integer inverse.

Note that any unsigned computer arithmetic instruction that has bit width w automatically gets performed modulo 2w. This is reflected in C and C++; the data types uint32_t and uint64_t respectively ensure arithmetic modulo 232 and 264.

# 3 Proof

Rearranging (3),
ax rsub {0} ` equiv ` 1 - y ` equiv ` 1 - y rsup { pow(2, `0) } ``` (mod 2^w)	(7)

Assume for an arbitrary value of integer n that
ax rsub {n} equiv 1 - y rsup { pow(2, `n) } ``` (mod 2^w)	(8)

Multiply both sides of (4) by a.
ax rsub {n+1} equiv ax rsub {n} ( 1 + y rsup { pow(2, `n)} ) ``` (mod 2^w)	(9)

Substitute (8) for axn .
ax rsub {n+1} ` equiv ` (1 - y rsup { pow(2, `n)}) ( 1 + y rsup { pow(2, `n)} ) ` equiv ` 1 - y rsup { pow(2, `n+1)} ``` (mod 2^w)	(10)

By induction, base case (7) and steps (8) (10) prove that for all n >= 0,
ax rsub {n} equiv 1 - y rsup { pow(2, `n) } ``` (mod 2^w)	(11)

Substitute (3) for y.
ax rsub {n} equiv 1 - (1 - ax rsub{0}) rsup { pow(2, `n) } ``` (mod 2^w)	(12)

By definition of congruence, there exists an integer q such that we can restate (2) as
ax_0 = 1 - q2^k	(13)

Substitute (13) into (12).
ax rsub {n} ` equiv ` 1 - (1 - (1 - q2^k)) rsup { pow(2, `n) } ` equiv ` 1 - q rsup { pow(2, `n) } 2 rsup { k `pow(2, `n) } ``` (mod 2^w)	(14)

Since (5) sets p = log2 (w / k) ,
ax rsub {p} ` equiv ` 1 - q rsup { pow(2, `p) } 2 rsup { k `pow(2, `log rsub{2}(w/k)) } ` equiv ` 1 - q rsup { pow(2, `p) } 2 rsup { w } ` equiv ` 1 ``` (mod 2^w)	(15)

Thus xp is the integer multiplicative inverse of a (mod 2w).

# 4 Relationship to Newton’s Method

We can show that the algorithm of Section 2 is closely related to Newton’s method.

Restating recurrence (4),
""x rsub {n+1} equiv x rsub {n} ( 1 + y rsup { pow(2, `n)} ) `` (mod 2^w) newline ""x rsub {n+1} equiv x rsub {n} ( 2 - (1 - y rsup { pow(2, `n)} )) `` (mod 2^w)	(16)

Substitute (11) into (16).
x rsub {n+1} equiv x rsub {n} ( 2 - ax_n ) `` (mod 2^w)	(17)

The recurrence for the multiplicative inverse via Newton’s method [10] is given as
x rsub {n+1} = x rsub {n} ( 2 - ax_n )	(18)

Taking this modulo 2w results in (17), and thus for all n, the Newton’s method recurrence
and Section 2’s recurrence (4) produce equivalent values modulo 2w (i.e. up to w bits).

# 5 Formulas to Set x0, with Proofs

Simply restating (2), we wish to find an integer x0 such that
ax_0 equiv 1 `` ( mod 2^k )	(19)

Formula 1 (k=1)
For k=1, set x0=1.
Proof:
Since a is an odd integer, a*1 equiv 1 `` ( mod 2^1 ) , and by substitution ax_0 equiv 1 ( mod 2^k) , which is congruence (19).
Formula 2 (k=2)
For k=2, set x0=a.
Proof:
Let the integer q=a/4, and the integer r=a%4. Thus
""``a=4q+r newline ""``a equiv r ``` ( mod 4) newline ""a^2 equiv r^2 `` ( mod 4)	(20)

Since a is odd, r belongs to the set {1, 3}. By testing every element of the set we see that
r^2 equiv 1 ` ( mod 4)	(21)

Thus by (20),
a^2 equiv r^2 equiv 1 `(mod 4)	(22)

Since a*a equiv 1 ` ( mod 2^2) , by substitution ax_0 equiv 1 ` (mod 2^k) .
This same approach can also show that for k=3, x0=a always satisfies (19). We focus on k=2 because k=3 is rarely needed.

Formula 3 (k=4 and w>=4)
For k=4, set x0=XOR((3a)%2w, 2). The formula is attributed to Peter Montgomery [4].
Proof:
Let the integer q=a/16, and the integer r=a%16. Thus
""phantom {a{*}} a=16q+r newline ""phantom {a{*}} a equiv r ``` ( mod 16)	(23)

Since a is odd, r belongs to the set {1, 3, 5, 7, 9, 11, 13, 15}. By testing every element of the set we see that
r*XOR(3r, 2) equiv 1 ` ( mod 16)	(24)

Using (23) with (24),
a*XOR(3r, 2) equiv 1 ` ( mod 16)	(25)

By (23) and the fact that w>=4,
`````````````````````````3a equiv 3r ` ( mod 16) newline (3a)%2^w equiv 3r ` ( mod 16)	(26)

Thus, the result of 3a % 2w must have the same value in its second bit as the result of 3r. We can observe that XORing an integer with 2 flips the second bit of the integer and leaves the rest of the integer unchanged. Since the results 3a % 2w and 3r both contain the same value at their second bits, both results will continue to have equal second bits after being XORed with 2, and the rest of their bits will be unchanged. Continuing from (26),
XOR((3a)%2^w, `2) equiv XOR(3r,` 2) `` ( mod 16)	(27)

Substituting (27) into (25),
a*XOR((3a)%2^w, 2) equiv 1 ` ( mod 16)	(28)

By substitution we can see that a*x_0 equiv 1 ` ( mod 2^k) , which is congruence (19).
This same approach can also show that for k=5, x0=XOR((3a) % 2w, 2) always satisfies (19).
Formula 4 (an alternate formula for k=4 and w>=4)
For k=4, set x0=(XOR(a, 2) – ((a+a)%2w))%2w.
This formula was found by brute force testing combinations of operators and integer constants across candidate formulas x0= (r op1 constant1) op2 (r op3 constant2), where r is a variable integer, and op1, op2, and op3 were any of the operators XOR, AND, OR, add, subtract, leftshift; a candidate formula for x0 was successful if it satisfied rx_0 equiv 1 ` ( mod 16 ) for all odd values r from 1 to 15.
Note that Formula 4 usually requires one more instruction to implement than Formula 3. An exception to this is usually SIMD implementations.
Proof:
Let the integer q=a/16, and the integer r=a%16. Thus
""phantom {a{*}} a=16q+r newline ""phantom {a{*}} a equiv r ``` ( mod 16)	(29)

Since a is odd, r belongs to the set {1, 3, 5, 7, 9, 11, 13, 15}. By testing every element of the set we see that
r`*`(XOR(r,2)–(r+r)) ` equiv ` 1 `` ( mod 16)	(30)

Using (29) with (30),
a`*`(XOR(r,2)–(a+a)) ` equiv ` 1 `` ( mod 16)	(31)

By (29), a equiv r ` ( mod 16 ) . Thus a must have the same value in its second bit as r. We can observe that XORing an integer with 2 flips the second bit of the integer and leaves the rest of the integer unchanged. Since a and r contain the same value at the second bit, both integers will continue to have equal second bits after being XORed with 2, and the rest of their bits will be unchanged. Thus a equiv r ` ( mod 16 ) implies that
XOR(a,2) equiv XOR(r,2) `` ( mod 16 )	(32)

Substituting (32) into (31),
a`*`(XOR(a,2)–(a+a)) ` equiv ` 1 `` ( mod 16)	(33)

And since w>=4,
a`*`(XOR(a,2)–(a+a)%2^w)%2^w ` equiv ` 1 `` ( mod 16)	(34)

By substitution we can see that a*x_0 equiv 1 ` ( mod 2^k) , which is congruence (19).

# 6 Efficiency

We compare in this section the expected number of CPU cycles to complete a 64 bit inverse (i.e. modulo 2w with w = 64), based on a performance model. We will also briefly consider throughput at the end of this section. For our performance model, we specify that an addition (or subtraction) requires 1 cycle to complete and that a multiplication requires 3 cycles to complete, and that multiplications are pipelined and that an addition can issue and execute in parallel with a multiplication. This model also specifies that the operation 3*a can be completed in one cycle (via an add with shift instruction, or the x86 LEA instruction), and that an XOR operation requires one cycle. This model roughly corresponds to x86 Intel CPU non-SIMD instruction timings from the last 12 years [15], and it reflects typical capabilities of modern CPUs.

Let’s implement Newton’s method [10] for the 64 bit inverse:

1. uint64_t newtons_inverse(uint64_t a)
2. {
3. assert(a%2 == 1);
4. uint64_t x0 = (3*a)^2; // See section 5, formula 3.
5. uint64_t x1 = x0*(2 - a*x0);
6. uint64_t x2 = x1*(2 - a*x1);
7. uint64_t x3 = x2*(2 - a*x2);
8. uint64_t x4 = x3*(2 - a*x3);
9. return x4;
10. }
  Figure 2: C code for the 64 bit inverse using Newton’s method.

Inspired by the example of Reynolds [8], let us consider the cycle timings of Figure 2 under the performance model we described. We will start on cycle 0 with 3*a. Operations are listed in order of the cycle on which they can issue. If more than one operation could issue on the same cycle, they would be listed on the same row, though we will see this never happens with Figure 2. Since every instruction in Figure 2 depends upon its preceding instruction, there is one long dependency chain throughout the Newton’s method algorithm:

Cycle number Operation(s)
0. tmp = 3*a (usually a single cycle operation)
1. x0 = tmp ^ 2 (^ is xor)
2. tmp = a*x0
3. (no instruction possible, waiting on tmp)
4. (no instruction possible, waiting on tmp)
5. tmp = 2 – tmp
6. x1 = x0 * tmp
7.
8.
9. tmp = a*x1
10.
11.
12. tmp = 2 – tmp
13. x2 = x1 * tmp
14.
15.
16. tmp = a*x2
17.
18.
19. tmp = 2 – tmp
20. x3 = x2 * tmp
21.
22.
23. tmp = a*x3
24.
25.
26. tmp = 2 – tmp
27. x4 = x5 * tmp
28.
29.
30. return x4

Let’s implement Dumas’ original Algorithm 3 [7] without looping for the 64 bit inverse:

1. uint64_t original_dumas_inverse(uint64_t a)
2. {
3. assert(a%2 == 1);
4. uint64_t y = a - 1;
5. uint64_t u0 = 2 - a;
6. y *= y;
7. uint64_t u1 = u0*(1 + y);
8. y *= y;
9. uint64_t u2 = u1*(1 + y);
10. y *= y;
11. uint64_t u3 = u2*(1 + y);
12. y *= y;
13. uint64_t u4 = u3*(1 + y);
14. y *= y;
15. uint64_t u5 = u4*(1 + y);
16. return u5;
17. }
  Figure 3: C code for the 64 bit inverse using Dumas’ algorithm 3.

Let’s consider the cycle timings for Figure 3, starting on cycle 0 with its subtraction a - 1. Operations are listed in order of the cycle on which they can issue, and when more than one operation can issue on the same cycle, they are listed on the same row:

Cycle number Operation(s)
0. y = a – 1
1. u0 = 2 – a, y *= y
2. (no instruction possible, waiting on y)
3. (no instruction possible, waiting on y)
4. tmp = (1 + y), y *= y
5. u1 = u0 * tmp,
6.
7. tmp = (1 + y), y *= y
8. u2 = u1 * tmp
9.
10. tmp = (1 + y), y *= y
11. u3 = u2 * tmp
12.
13. tmp = (1 + y), y *= y
14. u4 = u3 * tmp
15.
16. tmp = (1 + y)
17. u5 = u4 * tmp
18.
19.
20. return u5

There are two dependency chains (one for y and one for u) executing mostly in parallel. As a result Dumas’ algorithm completes in 20 cycles, compared to 30 cycles for Newton’s method.

And finally let’s consider the timings for our earlier Figure 1, which implemented the 64 bit inverse using the algorithm presented in this paper:

Cycle number Operation(s)
0. tmp = 3*a (usually a single cycle op)
1. x0 = tmp ^ 2 (^ is xor)
2. tmp = a*x0
3.
4.
5. y = 1 – tmp
6. tmp = (1 + y), y *= y
7. x1 = x0 * tmp
8.
9. tmp = (1 + y), y *= y
10. x2 = x1 * tmp
11.
12. tmp = (1 + y), y *= y
13. x3 = x2 * tmp
14.
15. tmp = (1 + y)
16. x4 = x3 * tmp
17.
18.
19. return x4

Compared to Figure 3’s timings, Figure 1 completes one cycle faster, mostly due to its ability to use the efficient formula 3 (or formula 4) from section 5. Under our performance model of a typical modern microprocessor, this paper’s algorithm (Figure 1) improves expected latency of the 64 bit inverse by ~60% over Newton’s method (Figure 2) and by ~5% over Dumas’ Algorithm 3 as presented in his paper (Figure 3).

We will briefly mention throughput, which unfortunately needs specific context to analyze. It depends not only on these functions, but largely upon surrounding code, data dependencies, and the CPU micro-architecture. Nonetheless, we may offer two cautious observations: If there is a loop-carried dependency on the result of the inverse, the lowest latency functions for the inverse might tend to help throughput. If a loop contains the inverse and has a large number of multiply operations, the resulting pressure on the CPU’s multiplication execution unit(s) may hinder throughput; in such a case, an inverse function with a low number of multiplies might help (this paper’s function and Newton’s method are tied for lowest number of multiplies).

# 8 Conclusion

Dumas’ algorithm for the inverse has a strong advantage over Newton’s method due to its ability to exploit instruction level parallelism (from pipelining and/or superscalar execution units) available in modern microprocessors. The algorithm in this paper expands upon Dumas’ work to allow for a more efficient starting value for its recurrence sequence, typically using Formula 3 from Section 5. This results in the lowest number of cycles currently known for calculating the multiplicative inverse of an integer (modulo 2w) on a computer, when w is less than or equal to the native bit width of a CPU’s arithmetic instructions.
# References

1. Wikipedia contributors. Montgomery modular multiplication. Wikipedia, The Free Encyclopedia. Revised December 17, 2019. https://en.wikipedia.org/w/index.php?title=Montgomery_modular_multiplication&oldid=931195404
2. Henry Warren. Hacker’s Delight 2nd Ed. [Section 10.16], Addison-Wesley, 2013.
3. Henry Warren. Hacker’s Delight 2nd Ed. [Section 10.17], Addison-Wesley, 2013.
4. Ernst W. Mayer. Efficient long division via Montgomery multiply. arXiv:1303.0328v6, 21 August 2016
5. Wikipedia contributors. Extended Euclidean Algorithm. Wikipedia, The Free Encyclopedia. Revised January 29, 2021. https://en.wikipedia.org/w/index.php?title=Extended_Euclidean_algorithm&oldid=1003613686
6. Wikipedia contributors. Newton’s Method. Wikipedia, The Free Encyclopedia. Revised January 25, 2020. https://en.wikipedia.org/w/index.php?title=Newton%27s_method&oldid=937542756#Multiplicative_inverses_of_numbers_and_power_series
7. Jean-Guillaume Dumas. On Newton-Raphson iteration for multiplicative inverses modulo prime powers. IEEE Transactions on Computers, August 2014. arXiv:1209.6626v5, 22 April 2019
8. Marc Reynolds. Integer multiplicative inverse via Newton's method. 18 September 2017, https://marc-b-reynolds.github.io/math/2017/09/18/ModInverse.html
9. Torbjörn Granlund and Peter Montgomery. Division by Invariant Integers using Multiplication. ACM SIGPLAN Notices, Vol. 29, No. 6, June 1994.
10. Henry Warren. Hacker’s Delight (1st Ed.), [Section 10.15], Addison-Wesley, 2002.
11. Ortal Arazi and Hairong Qi. On Calculating Multiplicative Inverses Modulo 2m. IEEE Transactions on Computers, Vol. 57, Issue 10, October 2008.
12. Çetin Kaya Koç. A New Algorithm for Inversion mod pk. IACR Cryptology ePrint Archive, 28 June 2017
13. Daniel Lemire. Computing the inverse of odd integers. 18 September 2017, https://lemire.me/blog/2017/09/18/computing-the-inverse-of-odd-integers/
14. Quentin Carbonneaux. “2019-01-15.” Notes 15 January 2019, https://c9x.me/notes/2019-01-15.html
15. Agner Fog. Instruction Tables Lists of instruction latencies, throughputs and micro-operation breakdowns for Intel, AMD, and VIA CPUs. Revised 2021-03-22. https://www.agner.org/optimize/instruction_tables.pdf
16. Jeffrey Hurchalla. Montgomery REDC using the positive inverse (mod R). 28 December 2020, https://github.com/hurchalla/modular_arithmetic/blob/master/montgomery_arithmetic/include/hurchalla/montgomery_arithmetic/low_level_api/detail/platform_specific/README_REDC.md